## Slide 1
CSE299.3 Group #1
Project Proposal
SimQC
A browser-based quantum circuit simulator with stepwise inspection and AI-assisted explanation
● Aoutul Nabi Purna
● Shishir Dhar
● Shihab Sharar
● Md. Iftikhar Alam Hrithik
Department of Electrical and Computer Engineering · North South University, Dhaka
Group 1 · CSE299.3: Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
01 / 15

## Slide 2
Team Introduction
Group 1 — Our Members
As required, we begin by introducing all group members with their full names:
AP
Aoutul Nabi Purna
aoutul.purna.241@northsouth.edu
Dept. of ECE · North South University
SD
Shishir Dhar
shishir.dhar.241@northsouth.edu
Dept. of ECE · North South University
SS
Shihab Sharar
shihab.sharar.241@northsouth.edu
Dept. of ECE · North South University
MH
Md. Iftikhar Alam Hrithik
iftikhar.hrithik.241@northsouth.edu
Dept. of ECE · North South University
Today we present SimQC — a browser-based quantum circuit simulator with stepwise inspection and AI-assisted explanation.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
02 / 17

## Slide 3
01 · Introduction
Why build another simulator?
Quantum computing introduces primitives with no classical equivalent — even small circuits behave in ways that are hard to predict by inspection.
GAP 1
Math ≠ intuition
Abstract linear algebra fails to build a real intuition about the actual mechanism behind circuits.
GAP 2
Hardware is out of reach
Without quantum hardware, a simulator is the primary tool for developing intuition and verifying algorithms.
GAP 3
Existing tools are heavy
Existing simulators vary widely, and many are tied to an SDK, a Python environment, or a server-side backend.
Our answer: a lightweight, browser-resident simulator — open a tab and simulate. Zero installation lets a learner focus on the circuit itself rather than on environment setup.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
03 / 17

## Slide 4
02 · Problem Statement
Intuition stops scaling at 2ⁿ
Hand computation works for small systems, but as qubits grow the state dimension grows exponentially, and multi-qubit behaviour — entanglement and the interference patterns of Grover and QFT — becomes impossible to verify by inspection.
2¹⁰
amplitudes at 10 qubits
2²⁰ ≈ 1 M
amplitudes at 20 qubits
2²⁴ ≈ 16.7 M
amplitudes at the 24-qubit cap
(i) REPRESENT
Explicit state representation
Multi-qubit states represented explicitly, as vectors of complex amplitudes.
(ii) APPLY
Targeted gate application
Gates applied efficiently to the targeted qubits only — never the entire system.
(iii) VERIFY
Canonical algorithms, verified
Quantum algorithms implemented through gates and checked against theory.
(iv) INSPECT
Inspect the journey, not just the result
Users see how a circuit produces its result — not only its final measurement.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
04 / 17

## Slide 5
03 · Related Work
Standing on the shoulders of Quirk
PRINCIPAL REFERENCE
Quirk — drag-and-drop, in-browser
▸ Open-source browser quantum circuit simulator (Apache-2.0, by C. Gidney)
▸ Drag-and-drop circuit grid with real-time simulation
▸ Inline state displays: probability, Bloch sphere, amplitude, density matrix
▸ URL serialization · undo/redo · support for controlled gates
HOW WE DIFFER
Inspiration — not imitation
▸ Quirk is our design inspiration — we do not copy its architecture.
▸ Quirk already displays state after every circuit column.
▸ SimQC therefore scopes to breakpoint-based, user-driven stepwise debugging — a debugger interaction model, not passive per-column display.
● Qiskit
● Cirq
● PennyLane
● IBM Quantum Composer
— powerful, but tied to Python/SDKs or server-side backends
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
05 / 17

## Slide 6
04 · Objectives & Scope
Seven committed objectives
01 · STATE
Explicit state vectors complex amplitudes, normalized after every gate; warning at 20 qubits, hard cap at 24.
02 · GATES
Gate library: minimum X, Y, Z, H, CNOT, Rx, Ry, Rz; extended set (I, S, T, CZ, SWAP, Toffoli) planned as an extension.
03 · EFFICIENCY
Target-only application: each gate applied only to its target qubits — the full 2ⁿ×2ⁿ unitary matrix is never materialized.
04 · MEASUREMENT
Repeated-shot sampling with state collapse.
05 · ALGORITHMS
≥ 3 canonical algorithms: Deutsch–Jozsa, Grover, Quantum Fourier Transform — verified against theoretical results.
06 · EDITOR
Custom drag-and-drop editor driving the simulation core through a clean interface.
07 · AI MODULES
Explainer AI — describes, breaks down, and simplifies existing circuits. Builder AI — synthesizes circuits from a textual description.
Honest scoping: the builder AI is a proposed feature, not a guaranteed deliverable — no accuracy claims. Performance is discussed asymptotically only; no benchmark numbers.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
06 / 17

## Slide 7
05 · Core Engineering Insight
Per-gate cost: O(2ⁿ), not O(4ⁿ)
TEXTBOOK CONSTRUCTION
O(4ⁿ) per gate
Lift G to the full 2ⁿ × 2ⁿ operator via Kronecker products, then apply it to the state:
Uₜ = I ⊗ ⋯ ⊗ I ⊗ G ⊗ I ⊗ ⋯ ⊗ I
▸ Materializes a dense 2ⁿ × 2ⁿ matrix
▸ Dense matrix–vector product for every gate
▸ Infeasible beyond small n
SIMQC APPROACH
O(2ⁿ) per gate
Uₜ only mixes amplitude pairs whose indices differ in bit t ( j = i ⊕ 2ᵗ ) — update each such pair directly:
( α′ᵢ , α′ᵢ⊕2ᵗ )ᵀ = G · ( αᵢ , αᵢ⊕2ᵗ )ᵀ
▸ 2ⁿ indices form 2ⁿ/2 disjoint pairs — the same 2×2 matrix G acts on each pair
▸ Controlled gates: the pair update is applied only when the control bits are 1
16.7 M
amplitudes at 24 qubits — stored in Float64Array
≈ 2.8 × 10¹⁴
entries in the full unitary — which is never built
≈ 8.4 M
tiny 2×2 pair updates per gate — perfectly feasible
This pairwise update is exactly the multi-qubit generalization of the single-qubit product, with the same 2×2 matrix G acting on a different amplitude pair per index.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
07 / 17

## Slide 8
06 · Methodology — States & Evolution
A small matrix mixes a small set of amplitudes
|ψ⟩ = ∑ αᵢ |i⟩ , i = 0 … 2ⁿ−1 , αᵢ ∈ ℂ (1)
∑ |αᵢ|² = 1 (normalization) (2)
|ψₖ₊₁⟩ = Uₖ |ψₖ⟩ (unitary update per gate / column) (3)
IMPLEMENTATION
Storage & arithmetic
▸ Amplitudes stored in JavaScript Float64Array typed arrays — real & imaginary parts interleaved or paired.
▸ Complex arithmetic implemented once and reused — the dependency order ensures no module duplicates it.
HADAMARD IN ACTION
H = 1⁄√2 · [ 1 1 ]
[ 1 −1 ]
G (α, β)ᵀ = ( g₀₀α + g₀₁β , g₁₀α + g₁₁β )ᵀ (4)
H|0⟩ = 1⁄√2 ( |0⟩ + |1⟩ ) — uniform superposition
The canonical pattern for every gate application: a small matrix mixes a small set of amplitudes, and the cost is proportional to the size of that set.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
10 / 17

## Slide 9
07 · Methodology — Measurement
From amplitudes to observed outcomes
P(i) = |αᵢ|² — Born rule (7)
STEP 1
Sampling & collapse
Measuring basis state |i⟩ yields outcome i with probability P(i), after which the state collapses to the sampled outcome.
STEP 2
Repeated-shot sampling
The draw is repeated across many shots; the empirical frequencies form the measurement histogram shown in the UI — the same view used to verify algorithms like Grover.
● shots: 1,024
● collapse → re-prepare per shot
|000⟩
|001⟩
|010⟩
|011⟩
|100⟩
|101⟩
|110⟩
|111⟩
Illustrative shot frequencies after amplitude amplification (e.g., Grover near peak)
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
11 / 17

## Slide 10
08 · Proposed Novel Features
Beyond a minimal simulator
FEATURE 1
Stepwise inspection with breakpoints
Place a breakpoint at any circuit column and execute step by step, observing the state after each gate — a debugger-oriented interaction model.
FEATURE 2
Reusable subcircuit blocks
Save any circuit as a single reusable block, internal state hidden behind a defined interface — even set breakpoints inside a subcircuit while paused.
FEATURE 3
Entanglement highlighting
Distinct visual cues mark qubit pairs or groups whose joint state is entangled — surfacing structure that amplitude vectors alone never show.
FEATURE 4
Input / output analysis
Select input and output lines on the flattened circuit; the AI analyses each input line independently, then explains how the per-input results combine.
FEATURE 5 — ONE MODULE, SWAPPABLE BACKEND
Explainer AI & Builder AI
Explainer: circuit → textual description. Builder: textual description → circuit.
Backend: the team's locally hosted model in Ollama — with the design kept swappable to a remote API. No statement is made about either model's accuracy or performance.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
08 / 17

## Slide 11
09 · System Architecture
The UI holds no mathematics
The UI issues high-level operations like “H gate on qubit 2 at column 4” — the core alone determines the mathematical meaning. The core is fully functional with no UI attached: the precondition for automated testing.
Frontend / UI
▸ Circuit Editor
▸ Gate Toolbox
▸ State Displays
▸ Debugger / Breakpoints
▸ AI Panel
Simulation Core
▸ Circuit Data Model
▸ Quantum State Engine
▸ Gate Library
▸ Execution Engine
▸ Measurement / Shots
▸ Algorithms — DJ · Grover · QFT
“H on qubit 2, column 4”
state vector, probabilities
● circuits serialize to JSON
● dependency order: complex → state → gates → executor → measurement
● headless core → script-driven tests
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
09 / 17

## Slide 12
10 · AI Circuit Analysis
How the AI reads a circuit
The explainer AI does not treat a circuit as a black box — it reads it the way the simulator does: flattened, gate by gate, junction by junction, all the way to the observed measurement.
STEP 1
Flatten the circuit
The AI sees the fully flattened circuit — any subcircuits present are decomposed into their individual gate logic.
STEP 2
Trace every qubit
Starting from each starting qubit, the AI follows it gate by gate through the whole circuit.
STEP 3
Analyze each junction
At every junction, the state is matched and analyzed — superposition, entanglement and phase.
STEP 4
Explain to measurement
The trace runs all the way to the observed measurement, grounding the explanation in real outcomes.
AIM — BUILDER AI AS THE NEXT STEP
From explaining to building
Mastering gate-level explanation is exactly the skill the Builder AI needs in reverse — turning a natural-language description into a working circuit.
HOSTED LOCALLY — OLLAMA
Local-first AI
The AI module runs on a locally hosted model in Ollama — all analysis stays on the team's machine. The design remains swappable to a remote API.
Grounded, not guessed: because the AI traces the real state evolution across every junction, its explanations reflect what the simulator actually computes.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
12 / 17

## Slide 13
11 · Validation Plan
Six hierarchical layers of proof
1
Complex arithmetic
Unit tests for scalar primitives — addition, multiplication, conjugation, modulus — against exact analytical values.
2
Canonical state transformations
H|0⟩, X|0⟩, Z|1⟩ must produce textbook state amplitudes.
3
State invariants & normalization
Every gate application preserves unitarity and norm conservation: |α|² + |β|² = 1.
4
Multi-qubit circuits & algebraic identities
Entanglement via Bell & GHZ circuits · H² = X² = I · quantum teleportation as a composite integration benchmark.
5
Algorithmic benchmarks
Deutsch–Jozsa, Grover, and QFT evaluated against known theoretical results — e.g., Grover's success rate at peak amplification.
6
Differential testing vs reference libraries
m = Σ kₒₚ arity factors × 6 amplitude composition profiles → 6m serialized test states executed and benchmarked against Qiskit & Cirq.
Headless core: every layer is exercisable by a script-driven test runner, with no manual interaction.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
13 / 17

## Slide 14
12 · Development Plan
Eight phases, bottom-up
PHASE 1
Architecture & data model
Fix the architecture and the data-model specification.
PHASE 2
Mathematical core
Complex numbers and the quantum state.
PHASE 3
Circuit engine & measurement
Execution engine, gate application, shots & collapse.
PHASE 4
UI + explainer AI begins
Minimal drag-and-drop editor; explainer AI development starts.
PHASE 5
Visualization
Probabilities, amplitudes, state-vector text, histogram.
PHASE 6
Algorithms
Deutsch–Jozsa, Grover, Quantum Fourier Transform.
PHASE 7
Persistence
Save & share circuits as JSON and via URL.
PHASE 8
Polish
Refinement, edge cases, and final presentation.
Math first, UI second — mirroring the core's dependency order, so each phase is testable on its own.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
14 / 17

## Slide 15
13 · Development Timeline
Eight weeks — mockup schedule from October 5
All eight phases distributed across an 8-week window starting October 5 — sequenced by dependency, bar length reflecting complexity. (Mockup)
W1
Oct 5
W2
Oct 12
W3
Oct 19
W4
Oct 26
W5
Nov 2
W6
Nov 9
W7
Nov 16
W8
Nov 23
P1 · Architecture & data model
1 wk
P2 · Mathematical core
2 wks
P3 · Circuit engine & measurement
2 wks
P4 · UI + explainer AI begins
2 wks
P5 · Visualization
2 wks
P6 · Algorithms — DJ · Grover · QFT
2 wks
P7 · Persistence — JSON · URL
1 wk
P8 · Polish
1 wk
Dependency-driven: each phase starts as soon as its prerequisite is in place — the mathematical core (W2–3) feeds the circuit engine (W3–4), and the algorithms (W6–7) need a working engine. Longer bars mark higher-complexity work.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
15 / 17

## Slide 16
14 · Conclusion
A virtual quantum lab in every browser tab
✓
Zero-install, zero-SDK — runs entirely client-side; no quantum hardware, no existing SDKs, no server runtime.
✓
O(2ⁿ) per gate — explicit state vectors with target-only gate application; the 2ⁿ×2ⁿ unitary is never built.
✓
≥ 3 canonical algorithms — Deutsch–Jozsa, Grover, and QFT, verified against their theoretical results.
✓
Custom drag-and-drop editor — drives a UI-free simulation core that is fully testable on its own.
✓
Novel contributions — breakpoint stepwise inspection, reusable subcircuits, entanglement highlighting, and an AI module with a swappable backend.
✓
Learning by building — the team gains deep understanding of quantum circuits and algorithms by implementing them from scratch.
Our vision: the perfect open-access, easy-to-use virtual laboratory — teaching the next generation of students and researchers, and supporting the current one.
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
16 / 17

## Slide 17
Thank you!
Questions & discussion are welcome — let's open the black box of quantum circuits together.
● Aoutul Nabi Purna
● Shishir Dhar
● Shihab Sharar
● Md. Iftikhar Alam Hrithik
{aoutul.purna.241, shishir.dhar.241, shihab.sharar.241, iftikhar.hrithik.241}@northsouth.edu
SimQC — Group 1 · CSE299.3 · North South University
Group 1 · CSE299.3 — Aoutul Nabi Purna · Shishir Dhar · Shihab Sharar · Md. Iftikhar Alam Hrithik
17 / 17